## Slide 1
PHONE + WEAR OS · VERSION 1.1.1 TEST
DreamSync
Dreams Redefined.
Designed to protect sleep continuity
Notes: Title. (~20s) Hi — this is Dream Sync, a research prototype that plays timed audio cues to the sleeping brain using just a phone and a smartwatch. In the next eight minutes I'll cover the problem it targets, the actual sleep science behind it, and — just as importantly — where the evidence runs out. This is deliberately an honest tour, not a sales pitch.

## Slide 2
The real risk is disturbing sleep
Cues can fragment the sleep they aim to help.
1
Sound can trigger arousal
Even quiet audio can increase movement or heart rate.
2
Wrist sensing is probabilistic
Motion and heart rate estimate likely sleep; they do not replace EEG.
3
Android needs an Arm action
One visible tap starts the night. Monitoring then runs automatically.
PROTECT
KEEP ASLEEP
When signals are weak, stale, or disturbed, DreamSync stays quiet.
DreamSync
2
Notes: The problem. (~50s) We spend about a third of our lives asleep, and for most people it's completely passive time — you can't observe it, let alone shape it. The stage that matters most for recovery and memory, deep slow-wave sleep, actually shrinks as we age. Meanwhile, sleep scientists have shown you *can* act on sleep — nudging deep sleep with sound, or cueing lucid dreams — but those techniques live in EEG labs with clinical hardware. The question Dream Sync asks: can the watch already on your wrist do a useful, safe version of that at home?

## Slide 3
Arm once; the rest is automatic
After a visible nightly Arm, the watch monitors and stays quiet unless strict gates pass.
Automatic likely-sleep detection
Stillness, heart-rate change, signal quality, and time of night estimate onset.
Quiet cue control
Arousal, stale sensors, off-wrist status, or low confidence blocks cues.
WATCH
Senses and protects
PHONE
Configures and reports
DreamSync
3
Notes: What it is. (~45s) It's a two-device system. The watch senses motion and heart rate, estimates your sleep stage, and decides when to cue. The phone sits by the bed and plays the actual audio at low volume. There are two interventions. Deep cues: paired pink-noise bursts during probable deep sleep. Lucid cues: a distinctive two-tone chime during probable REM. Each maps to a specific line of research — which is what the next three slides are about.

## Slide 4
Research shows timing matters
Acoustic cues can shift sleep physiology under controlled conditions.
1
Closed-loop results
Phase-locked cues strengthened slow oscillations in EEG-guided studies.
Ngo et al., 2013; 2015
2
Open-loop warning
Poorly timed open-loop stimulation produced a null memory result.
Weigenand et al., 2016
DESIGN IMPLICATION
TIMING FIRST
DreamSync uses conservative wrist-sensor gates, not EEG phase locking.
No memory claim. No guarantee. Stop at the first cue-linked arousal.
Peer-reviewed evidence · consumer prototype
DreamSync
4
Notes: The foundation — TMR. (~50s) The underlying principle is Targeted Memory Reactivation. In 2007, Rasch and colleagues paired a task with a rose smell, replayed the smell during deep sleep, and memory improved — with hippocampal activation on fMRI. Crucially it only worked in deep sleep, not REM or waking. In 2009, Rudoy showed the same with sound. And the 2020 meta-analysis of ninety-one experiments found a small but robust benefit, effect size 0.29 — real, in NREM only. So: cueing the sleeping brain is a genuine effect, not folklore. But note that word 'small.'

## Slide 5
Exact waveform, strict limits
A published paired-pulse pattern without a claim of EEG-level timing.
1
50 ms pink-noise bursts
Each cue is short and calibrated. Waveforms preload before arming.
Besedovsky et al., 2017
2
1.075 s onset spacing
Paired bursts are scheduled early after estimated sleep onset.
Nature Communications 8:1984
!
WHAT THIS DOES NOT MEAN
No EEG phase lock. No guaranteed deeper sleep, better memory, or uninterrupted sleep.
DOI: 10.1038/s41467-017-02170-3
DreamSync
5
Notes: Deep cues. (~55s) Dream Sync's deep cue rides on closed-loop acoustic stimulation. The founding 2013 study played two-click bursts locked to the slow oscillation's up-state and boosted both the brain waves and overnight word memory; out-of-phase clicks did nothing. A 2017 study replicated the physiology in older adults and roughly quadrupled recall versus sham. Now the honest caveat, on the right: the *physiology* replicates well — cues reliably move slow waves and spindles. The *memory* benefit does not. A 2023 meta-analysis pooled it at 0.14, not significant, with a clear decline as studies got better. So I present deep cues as a reliable physiological nudge with an unproven cognitive payoff.

## Slide 6
Learn the sleeper, then stay quiet
A seven-night rolling baseline adapts cautiously while safety gates stay in charge.
1
Seven-night baseline
Builds a personal pattern from motion, heart rate, timing, and signal quality.
Safe defaults are used on night one.
2
More signals when supported
IBI/HRV, temperature trend, and off-wrist data can improve confidence.
Samsung sensor layer remains gated.
!
SLEEP-FIRST RULES
No haptics during sleep. Stale data, off-wrist status, low battery, or low confidence disables cues.
Fail closed; never guess.
DreamSync
6
Notes: Lucid cues. (~55s) The lucid cue comes from targeted lucidity reactivation. The landmark 2021 study is genuinely stunning — across four labs, people in verified lucid REM sleep answered questions with prearranged eye movements. Real two-way communication with a dreaming person. And cue-replay methods have induced lucid dreams in about half of participants in lab naps. But the caveat matters: a systematic review found *no* induction technique works reliably, it's highly person-dependent, and that fifty-percent figure is a best-case morning nap, not a nightly at-home number. So this is a research-inspired prompt that may raise the odds for some people — framed exactly that way.

## Slide 7
Automatic after Arm; fail closed
DreamSync acts only after evidence lines up, then backs off at the first sign of waking.
1
Arm once
The user starts one visible nightly session.
2
Estimate onset
Stillness, heart rate, quality, and time identify likely sleep.
3
Require stability
Confidence must hold before an unexpired cue is allowed.
4
Stop on arousal
The first cue-linked wake signal disables cues for the night.
Protection flow: stable sleep → possible arousal → quiet recovery
Stable sleep
Possible arousal
Onset
~8 h
DreamSync
7
Notes: The engine. (~55s) Here's what makes it defensible rather than reckless. The watch estimates the stage from stillness, heart-rate features, and time-of-night priors. It requires the stage to hold stably, for minutes, inside the right window before it cues at all. Any movement or heart-rate spike ends the block and triggers a cool-down. And it self-limits: three cue-linked awakenings and it shuts cues off for the night. The chart shows why the time windows work — deep sleep front-loads the night, REM back-loads it, so even approximate timing is a reasonable bet.

## Slide 8
Compatibility follows capability
DreamSync checks model, sensors, software, permissions, and on-wrist status.
ULTRA
First validation:
Galaxy Watch Ultra 2024 and 2025
WATCH4+
Conditional support:
Galaxy Watch4–Watch8 families after self-test
CURRENT BOUNDARIES
Basic monitoring if full sensor gates fail. Apple Watch, Pixel Watch, Fitbit, and Garmin are not supported.
Apple Watch is a separate future Swift + HealthKit project.
DreamSync
8
Notes: The honest limit. (~50s) This is the slide I most want to land. Dream Sync reads motion and heart rate — not brain waves. Wearables like this are genuinely good, 85 to 95 percent, at telling sleep from wake. But at naming the actual stage they drop to roughly 60 to 85 percent — deep and REM get confused with light sleep. So timing cues by stage is a sound probabilistic bet, but some cues will land in the wrong stage. That's precisely why the app always says 'probable NREM' or 'probable REM' and never claims a diagnosis.

## Slide 9
Success means fewer disturbances
MEASURED TONIGHT
Awakenings
Wake after sleep onset
Longest uninterrupted bout
Cue-linked arousal rate
Morning disturbance
NOT CLAIMED
Guaranteed uninterrupted sleep
Medical treatment
EEG staging
Improved memory, deep sleep, or lucid dreaming
DreamSync
9
Notes: Potential effects. (~45s) Putting it together — what might this actually do? Plausibly: shift deep-sleep brain activity, raise lucid-dream odds for some users, and give a motivated person a real n-of-1 experimentation tool, since every night is logged. What it does *not* claim: a proven memory boost, reliable on-demand lucid dreaming, clinical staging, or any treatment. Keeping those two columns separate is the whole ethic of the project.

## Slide 10
Verified in code; hardware proof is next
1
LOCAL VERIFICATION
27 deterministic tests pass. Lint, signed bundles, and Android test packages compile.
2
INTERNAL TEST BUILDS
Phone 11 and Wear 12 are available to internal testers through Google Play.
3
STILL REQUIRED
Watch Ultra nights, fault tests, battery/audio checks, PSG validation, and a 12–20-night experiment.
Samsung SDK approval and provenance remain external gates.
No sleep-effect claim until controlled validation is complete.
DreamSync
10
Notes: Safety. (~45s) Risks, taken seriously. Any overnight audio can fragment sleep, so cues are low-volume, brief, user-calibrated to barely audible, and auto-disable after three cue-linked awakenings. Lucid-dream practice itself can disturb sleep, so windows are separated and cues capped. And there's a real caution: frequent lucid dreaming has been linked to higher dissociation in susceptible people, which warrants an in-app advisory. Bottom line on the bar: this is a research prototype, not a medical device.

## Slide 11
THE MISSION
Dreams Redefined.
Arm once. Detection stays automatic.
Stay quiet when confidence is low.
Stop after the first cue-linked wake signal.
Measure continuity before claiming benefit.
Research-informed. Stage-gated. Sleep-first.
Notes: Closing. (~25s) So, to close: a real problem — a third of life we can barely act on. An approach that brings two evidence-based techniques out of the lab and onto consumer hardware. An honest scope — strong on physiology, unproven on memory and lucidity, approximate on staging, and transparent about all of it. And a path forward: the nightly logs are the raw material for actually finding out what works. Thank you.